## Slide 1: Southern California Edison Vegetation Management Overview City of Sierra Madre
May 15, 2019

## Slide 2: Vegetation Management Program
Mission:
Further prevent risks to public safety and system reliability by managing vegetation in proximity to our electric facilities
Objectives:
Maintain a safe and reliable electric transmission and distribution system by using a defense-in-depth strategy to manage vegetation and minimize encroachments from vegetation, thus effectively managing the risk to public safety, vegetation-related wildfires, and vegetation-related outages that could lead to cascading

## Slide 3: Vegetation Management Team
Team:
20+ in-house certified arborists
Certified arborist tree inspection contractors
Notification consultants
800+ pruning contractors
Quality control oversight
Proudly serving SCE’s territory:
~900,000 trees inspected annually
~700,000 trees pruned per year; 400,000 trees in high fire risk areas
~ 39,000 dead, dying, diseased tree removals as prescribed

## Slide 4: Recent Conditions
“New abnormal” wildfire conditions have changed SCE vegetation management practices to protect public safety
What does this mean for you
Deeper pruning of trees and more trees pruned
  SCE’s pruning distances have increased (from ~6.5 ft. to 12 ft.), and will result in heavier pruning and more tree removals
    Distances consistent with California Public Utility Commission (CPUC) pruning distance guidelines
Increased tree removal where clearances cannot be met or obtained

## Slide 5: Program Overview
Program | Description | Criteria1
Distribution Vegetation Management Plan (DVMP) 69kV and below | Clear and maintain vegetation from Distribution lines per the new standards to prevent encroaching into the required clearance zones Removals are likely where clearances cannot be met/obtained | Clearance at time of pruning: 12’
Transmission Vegetation Management Plan (TVMP) 69kV and above |  | Clearance at time of pruning: 12’ (69kV) 30’ (115kV to 500kV)
Hazard Tree Management Program (HTMP) | Perform tree risk evaluation to identify hazard tree characteristics that can pose a risk to our electrical facilities | High Risk2 and within the Utility Strike Zone
Integrated Vegetation Management Plan (IVMP) | Strategies to promote desirable, stable, low-growing plants | SCE Rights-of-Way
2 Risk assessments are ranked by a tool that considers tree and site attributes to indicate possible hazardous conditions posed to equipment
1 Distances are consistent with CPUC recommended minimum clearances in General Order 95, Appendix E, Case 14

## Slide 6: Pruning Standards

## Slide 7: New Tree Pruning Standards
Chart: Old vs. New Standards
| Slow Growth | Medium Growth | Fast Growth
Old Standards | 6 | 8 | 10
New Standards | 6 | 4 | 2
In 2017, GO 05, Rule 35 Appendix E adopted new recommended minimal clearances at time of trim. These clearance requirements in high fire areas are 12’. Additional clearances may be required due to the factors below:
  Line dynamics
  Tree dynamics
  Tree characteristics
  Location
12’

## Slide 8: Tree Removal
Trees that represent a risk to SCE facilities and public safety
    Fast growing trees that cannot maintain compliance for 12 months
    Dead, dying or diseased trees
    Trees that cannot be pruned in accordance with ANSI A300 Tree Pruning Standards
  The removal is necessary to comply with the law and to ensure public safety
  Edison will remove/discard old trees and replace with new trees at no cost to the customers
  What should customers expect
  During pre-inspection, an SCE approved vendor will meet with the customer to explain the trees to be removed and obtain customers permission/signature prior to performing the work

## Slide 9: Candidate for Light Tree Pruning
Cutting branches, limbs and/or trunks 7” or less in diameter
  Old Standards: Cut between 6 ft. to 10 ft. (length varies due to tree growth rate)
  Aim to achieve: 12 ft. clearance for all trees
*Does not include Oaks, Conifers or Historical Trees
Before
After

## Slide 10: Candidate for Heavy Tree Pruning
Cutting branches, limbs and/or trunks 7” or greater in diameter
  Old Standards: Cut between 6 ft. to 10 ft. (length varies due to tree growth rate)
  Aim to achieve: 12 ft. clearance for all trees
*Includes Oaks, Conifers or Historical Trees
Before
After

## Slide 11: Candidate for Tree Topping
SCE follows best utility practices when pruning trees for public safety. In cases where a tree is growing directly under a power line and when there is no pruning alternative, SCE will cut through the trunk on the top of the tree – called topping -- to create a safety zone between the tree and the power lines. Property owners can opt to have SCE remove the tree instead.
Before
After

## Slide 12: Candidate for Tree Removal
Before
After

## Slide 13: Tree Topping
SCE follows best utility practices when pruning trees for public safety. In cases where a tree is growing directly under a power line and when there is no pruning alternative, SCE will cut through the trunk on the top of the tree – called topping -- to create a safety zone between the tree and the power lines. Property owners can opt to have SCE remove the tree instead.
The California Public Utilities Commission requires minimum clearances between vegetation and power lines at all times
Tree growth, storms and electrical demand can influence the distance between vegetation and power lines
Inadequate clearances can cause unplanned outage and create the potential of fire in the neighborhood
Right Tree Right Place

## Slide 14: City Map/Schedule
Months provided on the map are annual maintenance schedule performed by SCE approved contractor
Trees will be pre-inspected a month prior to scheduled work by SCE approved contractor
SCE Certified Arborists to perform quality control a month after tree prune/removals are complete

## Slide 15: Pruning Techniques Drive Notification
1 Customer permission obtained before work begun
Situation 1: “Light”
Criteria:
Meeting clearance standards requires cutting into branches, limbs and/or trunks 7” or less in diameter or up to 6’ beyond the old cuts
Customer Notification1:
SCE leaves door hangers with contractor contact information
  Notice #1: 30 days prior to work
  Notice #2: 48 hours prior to work
Situation 2: “Heavy”
Criteria:
Meeting clearance standards requires cutting into branches, limbs and/or trunks 7” or greater in diameter
Customer Notification1:
Notification Consultant makes contact with the customer via phone or in person to discuss plan
  Requires customer signature
  Door hanger 24-48 hours prior to work

## Slide 16: Customer Interface
Pre-Inspection
Notification Consultant
Prune/Remove
Final Inspection
Description
Resources
Schedule
Customer Interface
Perform tree assessment and write prescription
Approved Vendor
SCE Approves Work
~30 Days before scheduled work
1st Notification
1st Notification
Light Pruning
Pre-Inspection Contractor will leave door hanger describing proposed pruning work and indicate tree crew arrival (+30 days)
Heavy Pruning
For heavy tree work, the property owner will be contacted in person to discuss the tree pruning plan
2nd Notification
All Pruning
Tree Contractor will leave door hanger and indicate work will be performed within 24-48 hours
Make customer contact to discuss and coordinate work
SCE Approved Vendor
Tree crew performs work
24-48 Hours
Inspect work performed
SCE reviews work performed
Day after tree pruned/removed
SCE Approved Vendor
No Notification
Quality Control
No customer interruptions or contact

## Slide 17: Additional References

## Slide 18: Regulations and Requirements
Transmission & Distribution Codes and Regulations (All voltages)
CPUC: General Order 95, Rule 35
Cal Fire: Public Resource Code 4293*
Cal Fire: Public Resource Code 4292*
Cal Fire: Public Resource Code 4295.5*
Transmission Only Regulation (200kV and above)
NERC: FAC-003-4
*Applies to High Fire Threat Districts